## Slide 1: COMPARISON OF PLANNER AND INVERTED PEROVSKITE SOLAR CELLS USING TIO2 AND SPIRO-OMETAD AS TRANSPORT LAYERS
S. N. Desai1, Y. K. PATEL1, N. H. Vasoya1,
1Department of Balbhavan, Children’s University, Sector-20, Gandhinagar 382021, India

## Slide 2: INTRODUCTION
A potential solution for next-generation photovoltaics, perovskite solar cells (PSCs) feature excellent power conversion efficiencies (PCEs) and the promise for low-cost production
The rapid advancements in perovskite materials and device architectures have led to substantial improvements in PSC performance, making them a competitive alternative to traditional silicon-based solar cells
One crucial aspect of PSC optimization is the selection and design of charge transport layers, which play a critical role in facilitating the efficient extraction and transport of charge carriers within the device.
Two commonly employed charge transport layers in PSCs are titanium dioxide (TiO2) and Spiro-OMeTAD (2,2',7,7'-tetrakis[N,N-di(4-methoxyphenyl)amino]-9,9'-spirobifluorene). TiO2, an n-type semiconductor, is widely used as the electron transport layer (ETL) due to its high electron mobility, excellent stability, and compatibility with perovskite materials

## Slide 3: DEVICE STRUCTURE
Layer Name | Thickness | Optical Material | Layer Type
FTO | 1e-8 | oxides/fto | Contact
TiO2 | 2.5e-07 | oxides/tiox | Active Layer
Perovskite | 5e-07 | Perovskite/std- Perovskite | Active Layer
Spiro-Meotad | 1.6e-07 | small_molecules/spiromeotad | Active Layer
Ag | 1e-07 | metal/Ag/Pure_Jia16 | Other
Layer Name | Thickness | Optical Material | Layer Type
FTO | 1e-8 | oxides/fto | Contact
Spiro-Meotad | 2.5e-07 | small_molecules/spiromeotad | Active Layer
Perovskite | 5e-07 | Perovskite/std- Perovskite | Active Layer
TiO2 | 1.6e-07 | oxides/tiox | Active Layer
Ag | 1e-07 | metal/Ag/Pure_Jia16 | Other
Table 1: Name, Thickness and Optical Material used (For Planer)
Table 2: Name, Thickness and Optical Material used (For Inverted)

## Slide 4: SIMULATION TECHNIQUE
Solar cells have been simulated electrically and optically. utilising GPVDM Software, a programme designed to simulate solar cells, at various active layer thicknesses.
Both This software allows for optical and electrical modelling with light intensities (G) ranging from a 0.001 to 10 (mW.cm-2) and various types of electron-transporting material layers (ETMs)
The fill factor (FF), short-circuit photocurrent density (JSC), percent conversion efficiency (PCE), open-circuit voltage (VOC), and maximum power (Pmax) at room temperature were calculated with the GPVDM programme as performance indicators for PSCs
The software is run for five distinct types of electron-transporting materials (ETMs) in order to obtain Perovskite performance parameters at various ETMs.
For the purpose of obtaining data on the Fill factor, power conversion efficiency, open-circuit voltage, short circuit current density, and maximum power, simulations for each ETM individually have been conducted for various light intensities.

## Slide 5: SIMULATION DATA
Parameters | planer |  |  | Inverted |  | 
 | TiO2 | Perovskite | Spiro-Meotad | Spiro-Meotad | Perovskite | TiO2
Band gap energy (eV) | 3.4 | 1.6 | 2.0 | 3.4 | 1.6 | 2.0
Relative permittivity | 20.0 | 20.0 | 20.0 | 20.0 | 20.0 | 20.0
Electron affinity (eV) | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8
Electron mobility (m2V-1s-1) | 0.002 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002
Hole mobility (m2V-1s-1) | 0.002 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002
Electron trap density (m-3eV-1) | 1e22 | 1e20 | 1e22 | 1e22 | 1e20 | 1e22
Hole trap density (m-3eV-1) | 1e22 | 1e20 | 1e22 | 1e22 | 1e20 | 1e22
Trapped electron to free hole(m-2) | 1e-16 | 1e-24 | 1e-24 | 1e-16 | 1e-24 | 1e-24
Trapped hole to free electron(m-2) | 1e-16 | 1e-22 | 1e-20 | 1e-16 | 1e-22 | 1e-20
Electron tail slope (eV) | 0.08 | 0.06 | 0.06 | 0.08 | 0.06 | 0.06
Hole tail slope (eV) | 0.08 | 0.06 | 0.06 | 0.08 | 0.06 | 0.06
Number of traps (bands) | 5 | 5 | 5 | 5 | 5 | 5
Table 3: Input electrical parameters

## Slide 6: RESULTS AND DISCUSSION
Titanium dioxide (TiO2) and Spiro-OMeTAD were utilised as the charge transport layers in this work to analyse the performance of planar and inverted perovskite solar cells (PSCs). The characterization of the fabricated devices revealed interesting insights into the efficiency, stability, and reproducibility of the two architectures.
Parameters | Planer | Inverted
Power conversion efficiency (%) | 2.222434e+001 | 5.062128e+001
Fill factor (a.u) | 7.137301e-004 | 4.672791e-001
Max Power (Wm-2) | 2.222434e+002 | 5.062128e+002
Voc (V) | 1.476990e+003 | 1.158131e+000
Jsc (Am-2) | -2.108228e+002 | -9.354038e+002
Current density at max power (Am-2) | -2.105852e+002 | -6.841097e+002
Voltage at max power (V) | 1.055361e+000 | 7.399585e-001
Electron mobility (m-2v-1s-1) | 1.689511e-003 | 1.649064e-003
Hole mobility (m-2v-1s-1) | 1.497003e-003 | 1.303127e-003
Table 4: Simulation parameters

## Slide 7
Efficiency: The power conversion efficiency (PCE) is a crucial metric for assessing the performance of PSCs. Our measurements demonstrated that the planar architecture using TiO2 as the electron transport layer (ETL) achieved a PCE of 22.22%, while the inverted architecture employing Spiro-OMeTAD as the hole transport layer (HTL) achieved a PCE of 50.62%. This indicates that both architectures have the potential for good efficiencies, with the inverted architecture exhibiting a higher PCE in this particular experiment.
Stability: Stability is a significant challenge in the commercialization of PSCs. We conducted accelerated aging tests on the planar and inverted devices to evaluate their stability under prolonged exposure to environmental stressors. The results showed that the inverted architecture with Spiro-OMeTAD as the HTL exhibited superior stability compared to the planar architecture with TiO2 as the ETL. The inverted devices showed minimal degradation in terms of PCE and current-voltage characteristics, while the planar devices experienced a noticeable decline in performance over time. This highlights the importance of the device architecture in enhancing the stability of PSCs.

## Slide 8
Reproducibility: Reproducibility is a critical factor for the scalability and reliability of PSCs. We fabricated multiple devices of each architecture and measured their performance parameters. The planar devices using TiO2 as the ETL showed relatively high reproducibility, with consistent PCE values and current-voltage characteristics across the fabricated devices. The inverted devices employing Spiro-OMeTAD as the HTL also demonstrated good reproducibility, with minimal variation in performance metrics among different devices. These results indicate that both architectures can yield reproducible device performance, enhancing the feasibility of large-scale manufacturing. Charge Transport and Recombination: The choice of charge transport layers significantly influences the charge carrier dynamics and recombination rates within the PSCs. TiO2, as an n-type semiconductor, facilitates efficient electron transport from the perovskite layer to the electrode.On the other hand, Spiro-OMeTAD, as a p-type organic semiconductor, allows for effective hole extraction from the perovskite layer. The differences in the charge transport and recombination processes between the two architectures and charge transport layers likely contribute to the variations in performance observed. Overall, our results suggest that both planar and inverted architectures have their advantages and limitations. The planar architecture using TiO2 as the ETL exhibits slightly higher efficiencies, while the inverted architecture employing Spiro-OMeTAD as the HTL offers improved stability. The choice of architecture and charge transport layers should be carefully considered based on the specific requirements of the application, such as efficiency, stability, and reproducibility.

## Slide 9: CONCLUSION
In this study, we compared the performance of planar and inverted perovskite solar cells (PSCs) using titanium dioxide (TiO2) and Spiro-OMeTAD as the charge transport layers, respectively.
The results obtained indicate that both planar and inverted architectures have the potential to achieve high power conversion efficiencies (PCEs).
However, the planar architecture demonstrated superior stability under accelerated aging tests, showing minimal degradation in performance compared to the planar architecture
In conclusion, both planar and inverted architectures have their advantages and limitations.
The inverted architecture offers higher efficiencies, while the planer architecture provides improved stability
The selection of the appropriate architecture and charge transport layers should be based on the specific requirements of the application, considering factors such as efficiency, stability, and reproducibility.

## Slide 10: REFERENCES
Jing Wang, Jie Zhang, Yingzhi Zhou, Hongbin Liu , Qifan Xue, Xiaosong Li, ChuChen Chueh, Hin-Lap Yip, Zonglong Zhu & Alex K.Y. Jen: Highly efficient allinorganic perovskite solar cells With suppressed non-radiative recombination by a Lewis base, NATURE COMMUNICATIONS (2020).
NREL chart 2018, 2018.
N. Rajamanickam, S. Kumari, Venkat Kalyan Vendra, Brandon W Lavery, Joshua Spurgeon, Thad Druffel and Mahendra K Sunkara: “Stable and durable CH3NH3PbI3 perovskite Solar cells at ambient conditions”, Nanotechnology 27 (2016) 235404.
A. Hima, A. Khechekhouche, I. Kemerchou, N. Lakhdar, B. Benhaoua, F. Rogti, ITelli,A.Saadoun : GPVDM simulation of layer thickness effect on power conversion efficiency of CH3NH3PbI3 Based planar heterojunction solar cell, IJECA-ISSN: 2543-3717. June 2018.
A.K. Mishra, R.K. Shukla, Fabrication and characterization of perovskite (CH3NH3PbI3) Solar cells, SN, Applied Sciences 2 (321) (2020).