## Slide 1: A Comparative Study of the Scaled Boundary Finite Element Method (SBFEM) and the Finite Element Method (FEM)
Talkeshwar Ray1, Sukumar Baishya 2 and Dipika Devi3
1Assistant Professor, Department of Civil Engineering, Himalayan University, Itanagar, Arunachal Pradesh, India E-mail: raytalkeshwar@yahoo.com
2 Professor, Department of Civil Engineering, North Eastern Regional Institute of Science and Technology, India E-mail: sukumar.baishya@gmail.com
3Associate Professor, Department of Civil Engineering, North Eastern Regional Institute of Science and Technology, India E-mail: dipikace.nerist@gmail.com

## Slide 2
The Finite Element Method (FEM) has long been regarded as a robust numerical method for solving partial differential equations (PDEs) in engineering, particularly in solid mechanics, fluid dynamics, and heat transfer.
However, the emergence of the Scaled Boundary Finite Element Method (SBFEM) has provided an alternative approach, particularly effective in addressing certain limitations inherent in FEM. SBFEM, developed by Wolf and Song in the late 1990s, is a semi-analytical approach that combines elements of both FEM and boundary element methods (BEM), offering advantages in modeling unbounded domains and handling singularities.
This paper aims to explore the differences between these two methods in terms of their mathematical formulation, computational complexity, accuracy, and practical applications.
While FEM is well-established and widely adopted, SBFEM is gaining traction due to its capability in addressing certain types of problems more efficiently.
This comparison will help engineers and researchers understand when SBFEM may be a better choice over FEM and vice versa.
INTRODUCTION

## Slide 3
METHODOLOGY
Mathematical Formulation: The mathematical formulation of the Finite Element Method (FEM) and the Scaled Boundary Finite Element Method (SBFEM) begins with discretizing the governing equations for structural mechanics problems, typically described by partial differential equations (PDEs) derived from continuum mechanics.
  FEM Mathematical Formulation: Within each finite element, the solution (e.g., displacement, stress) is approximated by shape functions, which are typically low-order polynomials. The solution is expressed as:
Where, 𝑢(𝑥) is the approximated displacement, 𝑁𝑖(𝑥) are the shape functions, and
𝑢𝑖 are the nodal values of the unknown variable (e.g., displacements).
  SBFEM Mathematical Formulation: The discretized boundary in SBFEM leads to a system of equations in the form:
Where, 𝒓 is the radial distance and 𝜽 represents the tangential coordinates. The matrices [𝑨], [𝑩], [𝑪] depend on the boundary conditions and the geometry of the problem.

## Slide 4
b) Computational Aspects
FEM
  Mesh Generation: In FEM, a mesh is created over the entire domain, dividing it into finite elements.
  Handling of Boundary Conditions: Boundary conditions in FEM are applied directly to the nodes on the boundary.
  Solution Algorithm: FEM typically leads to a system of algebraic equations, which are solved using numerical techniques such as direct methods (e.g., Gaussian elimination) or iterative methods (e.g., conjugate gradient).
SBFEM
  Mesh Generation: Unlike FEM, SBFEM discretizes only the boundary of the subdomains, not the entire domain.
  Handling of Boundary Conditions: SBFEM simplifies the application of boundary conditions, as they are applied to the boundary of the subdomains.
  Solution Algorithm: SBFEM results in a semi-analytical solution for the radial direction, while the tangential direction is treated numerically.

## Slide 5
c) Practical Applications
FEM Applications: FEM is widely used in a variety of engineering fields for solving problems related to structural mechanics, fluid dynamics, heat transfer, and more. Some typical applications include:
Stress analysis in structures: FEM is used extensively to calculate stress, strain, and deformation in structures under various loading conditions.
Vibration analysis: FEM is used to calculate natural frequencies and mode shapes in mechanical and civil engineering systems.
Thermal analysis: FEM is applied to solve problems involving heat transfer in solid bodies, including conduction, convection, and radiation.
SBFEM Applications: SBFEM excels in specific applications where FEM might struggle, such as problems with singularities, unbounded domains, or highly complex geometries. Some typical applications include:
Crack propagation: SBFEM is particularly useful for fracture mechanics problems because it handles stress singularities at crack tips more efficiently than FEM.
Soil-structure interaction: In geotechnical engineering, SBFEM can model infinite domains (e.g., soil extending to infinity) without artificial truncation of the domain, as is required in FEM.

## Slide 6: COMPARATIVE ANALYSIS: SBFEM VS FEM
1. Mathematical Formulation
The FEM discretizes the entire domain into small finite elements, where the solution is approximated over each element. In FEM, the domain is subdivided into small finite elements, and the governing equations are solved for each element. The accuracy of FEM depends on the number and quality of the elements. Typically, FEM is used to solve a wide variety of boundary value problems, and it excels at providing accurate solutions for complex geometries with well- defined boundaries.
2. Mesh Generation
One of the key differences between FEM and SBFEM is in mesh generation. FEM requires a fine mesh throughout the entire domain to achieve high accuracy, particularly in regions of high stress gradients or where singularities are present. This can result in a significant computational cost, especially in three-dimensional problems.
3. Singularities and Infinite Domains
FEM struggles with singularities, such as stress concentrations at crack tips or sharp corners. To capture these singularities accurately, FEM often requires mesh refinement in the regions surrounding the singularity, which increases the computational cost.

## Slide 7
4. Handling Boundary Conditions
In FEM, boundary conditions are applied directly to the nodes on the boundary of the mesh. For complex boundary geometries, generating an appropriate mesh that aligns with the boundary conditions can be challenging and time-consuming. SBFEM simplifies the application of boundary conditions by discretizing only the boundaries of the subdomains. This allows for greater flexibility in handling complex boundary geometries and reduces the difficulty of mesh generation. Additionally, SBFEM naturally incorporates boundary conditions at infinity, making it more efficient for problems with unbounded domains.
5. Computational Efficiency
FEM is generally computationally intensive, especially for three-dimensional problems or problems with complex geometries. The need for fine meshing in regions of high stress gradients or singularities increases the computational effort, both in terms of memory usage and solution time.
6. Accuracy and Convergence
Both FEM and SBFEM are capable of providing accurate solutions to engineering problems. However, the accuracy of FEM is highly dependent on the quality and density of the mesh, particularly in regions of high stress gradients or singularities. In cases where the mesh is not sufficiently refined, FEM may produce inaccurate results.

## Slide 8
The results from the comparative study demonstrate the strengths and weaknesses of both methods.
In benchmark tests involving stress analysis in complex geometries and unbounded domains, SBFEM outperforms FEM in terms of computational efficiency, requiring fewer elements to achieve the same level of accuracy.
Additionally, SBFEM's ability to handle singularities and infinite domains without extensive mesh refinement makes it a more efficient option for certain types of problems.
However, FEM remains a robust and versatile method, particularly for problems with well- defined boundaries and regular geometries.
In such cases, FEM provides highly accurate results with well-established algorithms and software implementations.
RESULTS

## Slide 9
The comparison between SBFEM and FEM highlights the advantages and limitations of each method.
FEM is a well-established and versatile numerical method that excels in solving a wide range of engineering problems, but it requires fine meshing and can be computationally expensive for problems involving singularities or infinite domains.
SBFEM, on the other hand, offers a semi-analytical approach that provides significant computational advantages in problems involving complex geometries, singularities, and infinite domains.
Its ability to achieve high accuracy with fewer elements makes it an attractive alternative to FEM in certain applications.
However, SBFEM is not yet as widely adopted or implemented in commercial software as FEM, which may limit its accessibility to engineers and researchers.
Future research and development of SBFEM could lead to wider adoption of the method, particularly in large-scale engineering problems where computational efficiency is a key factor.
CONCLUSION

## Slide 10
Song, C. and Wolf, J.P. (1997). "The Scaled Boundary Finite Element Method – A Primer: Derivation, Advantages, and Applications." International Journal for Numerical Methods in Engineering.
Zienkiewicz, O.C., Taylor, R.L., and Zhu, J.Z. (2005). The Finite Element Method: Its Basis and Fundamentals. 6th Edition. Elsevier.
Wolf, J.P. (2003). The Scaled Boundary Finite Element Method. John Wiley & Sons.
Liu, G.R. and Quek, S.S. (2003). The Finite Element Method: A Practical Course. Butterworth-Heinemann.
Cheng, A., and Detournay, E. (1988). "Application of Boundary Integral Equations to Unbounded Domains." Advances in Boundary Element Methods.
REFERENCES

## Slide 11
Thank You