## Slide 1: RP-HPLC METHOD DEVELOPMENT AND VALIDATION FOR SIMULTENEOUS ESTIMATION OF DAPAGLIFLOZIN, GLIMEPIRIDE AND METFOMIN IN FIXED DOSE COMBINATIONS
Name : Anshika Bhatnagar1*, Bhuvnesh Kumar Singh1, Mandeep Kumar Gupta1, Sudhansu Ranjan Swain1
1Moradabad Educational Trust Group of Institutions Faculty of Pharmacy, Moradabad-244001, Uttar Pradesh, India.
Email for correspondence: anshikabhatnagar1299@gmail.com

## Slide 2
ABSTRACT
A simple, accurate, specific and precise method is developing for the simultaneous estimation of Dapagliflozin, Glimepiride and Metformin in fixed dose combination.
High performance liquid chromatography model name is Systronics (SYS LC-138), Chromatographic column is a Vertex C18, 4.6 X 250 mm, 5μm, UV Spectrophotometer (SHIMADZU UV-19001), digital pH meter, Ultra sonicator and Analytical balance (d & d scale) is used for method development and validation.
Drug samples are obtained from SYNOKEM Pharmaceuticals limited. Fixed dose combination sample of Dapagliflozin, Glimepiride and Metformin is collected from market with strength of 10 mg/1mg/500 mg respectively.
The sample solution is scan into UV Spectrophotometer between 200-400 nm range to identify the exact wavelength at which the sample shows maximum absorbance through detector. Dapagliflozin, Glimepiride and Metformin shows maximum absorbance at 248 nm in UV Spectrophotometer.
Reverse phase High Performance Liquid Chromatography (RP-HPLC) is used in this estimation. In method development, Phosphate buffer with pH 3 by OPA and Acetonitrile is used as mobile phase. Standard substances are dissolved first in 90 ml of Methanol, 10 ml of Water and 2 ml of Triethylamine.

## Slide 3
Chromatographic column is use to separate the components from mixture. UV-detector is assembled in Systronics HPLC to detect the samples.
The flow rate of mobile phase is maintained at 1 ml/min and the injection volume of sample is 20 μl. concentration of mixture of the sample is 50 μg/ml.
Developed method will validate through ICH guidelines Q2 (R2). It considers the factors like System suitability, Linearity, Precision, Accuracy, Specificity, Robustness, Limit of detection and Limit of quantification.

## Slide 4
THANK YOU